Tender Descriptive:

- PONZI LOWERED ARCH TOS -

CURVED DOOR OF CIRCUMFERENCE SECTOR AND AUTOMATIC OPENING

CURVED DOOR WITH CIRCUMFERENCE SECTOR PONZI LOWERED ARCH

Made of four mirrors with circumference sectors, curved to perfect radius, of which the fixed side panels and the central ones that open automatically to slide with mechanism PONZI STA 20.

The fixed and sliding side doors are built in 20 mm aluminium profiles, finishing surface made with fire - retardant RAL colour treatment (to be chosen by our wad), 8/9 mm thick laminated accident-prevention glass composed of two 4 mm clear 4 mm clear float plates with interposed pvb film from mm. 0.76. Special sealing gaskets with relative counter-profiles. The mechanism consists of: DSTA type microprocessor, mounted on a self-supporting steel support; suspension with carriages on high-slip ball bearings; Lauramid outer crown; transmission realized by means of a toothed belt in special

canvas rubber. Curved external skirt H = mm 220 covering the beam and the sliding track.

The automatism consists of:

•  N. 1 Gear Motor

•  N. 1 Transformer, power supply (220 / V-50 HZ. In input, 24V operation)

•  N. 1 Micro authorizing offrcer (program card)

•  N. 1 extruded aluminum track.

•  N. 1 Standard function selector (BDE)

•  N. 2 Movement and presence sensors.

•  N. 1 Emergency battery (guarantes 1 opening of the doors in case of power failure)

•  N.1 Locking with electric lock operated by the selector

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it