Tender Descriptive:

- PONZI AST -

PONZI AST AUTOMATIC SLIDING DOOR

Made in a single mirror that opens automatically. The door is complete with:

• jambs on three sides, with complementary extruded profiles that can be coupled together, suitable for wrapping the entire shoulder of the wall up to a thickness of 150 mm (for higher wall thicknesses it will be compensated separately with extra charge)

• 50 mm extruded aluminium alloy profiles - our rounded accident-prevention series surface finish made with an oven-painted or anodic electro-colouring treatment (colour to choose from our sample book)

• 40 mm thick panel with internal core (interspace) of high-density self-extinguishing Class 1 non-toxic polystyrene, double coating of plastic laminate, colored and supported by a chipboard or 4 mm MDF (standard Abet color)

The automatism consists of:

• N. 1 Low voltage gear motor.

• N. 1 Stabilized power supply.

• N. 1 Microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrier trolleys for door.

• N. 1 adapter profile for suspension leaf.

• N. 1 Multi-function battery pack

• N. 1 bistable electric lock.

Inspectable box in extruded aluminum (sh = 155 mm).

• N. 1 Function selector with 5 positions (KS).

• N. 2 Presence radar VIO ST

• N. 2 Elbow buttons

N. dimensions da mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it