Tender Descriptive:

- PONZI ALU FRAME PARALLEL -

MANUAL SLIDING HOSPITAL DOOR ALU FRAME PARALLEL

MANUAL SLIDING HOSPITAL DOOR ALU FRAME PARALLEL

Made in ONE leaf. Built with extruded profiles in ENAW 6060 aluminum alloy according to UNI 9006/1 rules and accessories belonging to the ALU PONZI system.The profiles will be anodized, silver color ARS1,

class 15 micron according to the UNI4522 regulation.

The door is complete with:

• Filling on three sides, with complementary extruded profiles that can be coupled together, suitable for wrapping the entire shoulder of the wall for a thickness from 100 to 150 mm (for higher wall thicknesses it will be compensated separately with extra charge).

• Door leaf, surrounded on all four sides by an aluminum frame with rounded edges of 45/50 mm; panel with internal core in high-density self-extinguishing Class 1 non-toxic polystyrene, double coating in HPL plastic thickness 0.9 mm, supported by a 4 mm MDF slab.

• Accessories: hook lock with Yale type cylinder, pair of round handle diameter 35 recessed on the upright

• Double door gasket in EPDM elastomer

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it