Tender Descriptive:

- PONZI RONDA -

RONDA TYPE ENTRY

UNION OF TWO CURVED DOORS: PONZI RONDA

Ronda type entrance compass composed of two automatic sliding doors of the swallow type coupled together to form a compass, each of which is constructed as follows: automatic sliding door is 20 swallow made with doors with circumference sector, of which the two central sliding automatically and the two parts fixed side panels. The fixed side doors are made of jansen-type steel sections of mm. 40, the central sliding doors in special extruded aluminium sections of 20 mm and curved to perfect radius, surface finish made with fire-retardant ral colour treatment (to be chosen from our sample book) 9/10 accident-prevention laminated glass composed of two slabs clear transparent float from mm. 4 + 5 with terposed film p.v.b. from mm. 0.76. Supporting structure made of curved and thermo-lacquered tubular steel with external veil h = mm 225 inspectionable drop-down box

in pre-painted alucobond sheet - white colour - thickness mm. 4 (suitable for inserting spotlights to be supplied to your care).

The Rondina microprocessor-controlled mechanism, with a basic automatic mechanism with rubber support on

LAURAMID guide wheels and silent sliding toothed belts, consists of:

•  N. 1 Gear Motor

•  N. 1 Transformer, power supply (220 / V-50 HZ. In input, 24V operation)

•  N. 1 Micro authorizing offrcer (program card)

•  N. 1 extruded aluminum track.

•  N. 1 Standard function selector (BDE)

•  N. 2 Movement and presence sensors.

•  N. 1 Emergency battery (guarantes 1 opening of the doors in case of power failure)

•  N.1 Locking with electric lock operated by the selector

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it