Specifications description:

- PONZI FDA BASIC MONOLATERAL -

AUTOMATIC FOLDING DOOR

• N. 1 Gearmotor.

• N. 1 Transformer, power supply.

• N. 1 Micro computer (program card).

• N. 1 Extruded aluminum track.

• N. 1 Programmable function selector (BDE).

• N. 2 combined radars (motion and presence sensor).

• N. 1 Emergency battery (guarantees the opening of the doors in the event of a power failure).

• N. 1 Locking with electric lock operated by the selector. Sliding accessories.

• Inspectionable box in extruded aluminum H = mm. 180.

Made of two folding leaves that can be opened automatically on one side only.

The leaves will be built with extruded aluminum alloy profiles - surface finish made with anodic electro-coloring treatment or fired paint (color of your choice from our sample book), complete with upper and lower pins rotating on ball bearings and special very high hinges resistance and tightness; safety stratified glass 55 mm 10/11 thick composed of two clear transparent float sheets of mm. 5 with interposed film p.v.b. from mm. 0.76. Perimeter gaskets for a perfect thermo-acoustic seal. Microprocessor-regulated folding door mechanism, mounted on aluminum support, internal lever system mounted on low-noise ball bearings, 220 / V 50Hz power supply,funzionamento a 24V.

The automation consists of:

AUTOMATIC FOLDING DOOR FDA BASIC MONOLATERAL