Tender Descriptive:

- PONZI PST L -

PONZI PST L ALUMINUM SLIDING DOOR

PST L LAMINATED SLIDING DOOR

Door equipped with sliding movement in opening and closing. Made in one / two doors.

The door consists of:

•Fixed wall-covering frame (gaps) perimeter on the three sides of the standard thick doorway for walls of mm. 150, built in aluminium sheet;

•Door compartment cover frame, made of special extruded aluminium alloy profile specially designed for specific use, standard finish anodized natural silver; suitable for inserting safety photocells during closing;

•Door thickness mm. 60 built with perimeter frame in special extruded aluminum alloy rounded profiles specially designed for specific use, natural silver anodized standard finish, complete with:

•Self-supporting panel with a coplanar sandwich structure made of two sheets of 8/10 stainless steel AISI 304 satin-finished sheet; two 5 mm MDF sheets; internal core in high density expanded polystyrene, insulating, soundproofing, self-extinguishing and Class 1 fire resistance.(For doors with a passage greater than 1200 mm, the plastic and / or stainless steel laminate will have a vertical junction line, whose position will be univocally and irrevocably determined by the construction constraints of the door panel);

•Perimeter gaskets on the four sides made of EPDM type elastomer;

The sliding and guide mechanism is made with:

• Specially designed upper rail extruded in special aluminum alloy prepared for wall mounting, natural silver anodised finish;

• Two steel carts with large nylon 6.6 wheels mounted on double ball bearings, with height, depth and anti-derailment adjustment

• Special skids on the ground with double cone offset (opening side) and single cone (closing side) made of anti-friction and anti-wear plastic material mounted on a stainless steel plate, for perfect sliding and guiding of the door.

• Composite cover casing, specially designed with rounded dust-proof profile and built with aluminium profiles ;

The door in the automatic version includes a specially designed and built automation for sliding doors of the HERMETIC type, complete with:

•  Low voltage electric gear motor with high mechanical reversibility complete with 2-channel optical encoder for position, speed and acceleration detection;

• Microprocessor control board with specific software that automatically manages acceleration, translation, approach and braking according to the weight of the leaves and the surrounding conditions;

• Electronic anti-crushing system both in closing and in opening, with triple control integrated in the control card and complying with the dictates of current regulations;

• Toothed belt transmission system made of neoprene coated in anti-wear and anti-friction material and reinforced with fiberglass / kevlar inserts;

•  Stabilized and filtered 200 W power supply;

•  Supply voltage 230V - 50 Hz - 24 Volt continuous current operation;

•  Control units for opening: n. 2 elbow buttons;

•  Safety sensors for protection in closing: n. 2 active infrared type presence sensors.

N. dimensions da mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it