Tender Descriptive:

- FDA BASIC -

AUTOMATIC DOOR WITH FOLDING SIDE COLLECTIONS

FDA BASIC FOLDING AUTOMATIC DOOR

Made of four folding doors that open automatically (two on each side).

The doors will be constructed with extruded aluminium alloy profiles- surface finish made with anodic electro-coloring treatment or fire painted (color to choose from our sample book) , complete with upper and lower pivots rotating on ball bearings and special very high hinges strength and tightness; 55 mm thick laminated anti-accident laminated glass composed of two clear transparent mm float plates 5 with interposed film p.v.b from mm 0,76. Perimeter seals for a perfect thermo-acoustic seal. Mechanism for folding door controlled by a microprocessor, mounted on aluminium support, internal lever system mounted on higly silent ball bearings, 220 / V 50 Hz  power supply, 24 V operation.

The automatism consist of:

•  N. 1 Gear motor.

•  N. 1 Transformer, power supply.

•  N.1 Microprocessor (programme card)

•  N.1 Extruded alumium track.

•  N.1 Programmable function selector (BDE)

•  N.2 combined radar (motion and presence sensors)

•  N.1 emergency battery (guarantees the opening of the doors in the absence of current)

•  N.1 Locking with electric lock operated by the selector.

•  Sliding accessories.

•  Inspectable box in extruded alumium H = mm. 180

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it