Tender Descriptive:

- PONZI ALU PANEL -

SWING HOSPITAL DOOR ALU PANEL

HOSPITAL SWING DOOR ALU PANEL ANTI RX

SWING DOOR PONZI ALU RX TYPE made in ONE / TWO swing leaves. Built with extruded profiles in ENAW 6060 aluminum alloy according to UNI9006/1 rules and accessories belonging to the ALU PONZI system. The profiles will

be anodized, silver color ARS1, class 15 micron according to UNI4522 regulation.

The door is complete with:

• Filling on three sides, with complementary extruded profiles that can be coupled together, suitable for wrapping the entire shoulder of the wall for a thickness from 100 to 150 mm (for higher wall thicknesses it will be compensated separately with extra charge), with inserted shielding in primary lead plates in thicknesses of 1, 2 or 3 mm.

• Door leaf, made of 45 mm thick self-supporting panel with 0.9 mm thick HPL plastic laminate , bordered on all four sides with visible hard wood finishes and / or colored PVC element or plastic laminate or aluminum element, with inserted shielding in primary lead plates in thicknesses of 1, 2 or 3 mm.

• Accessories: hook lock with Yale type cylinder, pair of round diameter 35 handle recessed on the upright

• Double door gasket in EPDM elastomer

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it